## Slide 1: Introduction to the Waste Impact Calculator
Notes: Hi, I’m Martin from the Oregon Department of Environmental Quality, and in this presentation I’m going to give you an introduction to the Waste Impact Calculator project.

## Slide 2: Outline
The “big problem” WIC addresses
What it is
Who it’s for
How it works
Ways to use it
What it leaves out
Alternatives
Notes: I’m going to tell you the context for this project – that is, the “big problem” that the Calculator addresses.
I’ll tell you what the Calculator does, who it’s for, how it works, and ways you can use it.
I’m also going to tell you about some important things that the Waste Impact Calculator leaves out. Every model has limitations, and to use the model wisely, you need to know what those limitations are. I’ll mention a few alternatives.

## Slide 3: The problem of waste
Notes: The context for the Waste Impact Calculator project might be called “the problem of waste.”
Throughout the past 50 or 60 years solid waste has been seen as a problem. But our perceptions of how waste is a problem has evolved.
Back in the 70s, when this picture was taken, there was a sense that waste represented a squandering of resources, but the main civic concern was that there was literally not enough room to store garbage.
More recently, there has been a lot of concern about trash that has been mishandled, and gets into aquatic environments, where it harms wildlife.
Finally, over the past 20 or 30 years there’s been a growing awareness of another kind of environmental harm. All that trash we see – whether it is being handled correctly or not – has to come from somewhere. It has to be created and used before it’s thrown away. And all those processes create environmental impacts like greenhouse gas emissions.
So all this trash you see is kind of just the tip of the iceberg in terms of environmental effects.
It is this third problem that the Waste Impact Calculator is concerned with.

## Slide 4: Weight vs. impact views of waste
Notes: To get into this a little bit deeper, I need to describe two different ways of perceiving and measuring waste.

## Slide 5: Weight based views of waste
Notes: The traditional way of looking at waste is to just quantify how much of it there is when you collect it. So for example there are trucks that pick waste up from your curbside and take it to landfill or recycling.

## Slide 6: Weight-based statistics and goals
Notes: These activities translate into statistics. Waste generation is the total weight of stuff in both kinds of bins. And the recycling, recovery, or diversion rate is a percentage – the amount of stuff in the recycling bin divided by the total generation.
Now rules for what gets counted in each of these bins can vary from place to place, but the idea remains the same.
Governments tend to set rules or goals encouraging more recycling or diversion, and sometimes less generation.

## Slide 7: What weight misses: environmental impacts
Notes: Weight based measurements are attractive and easy to do, because it’s easy to drive a truck onto a scale. However, this weight-based view misses something important: environmental impacts.
When that truck comes to get your stuff and take it to the landfill or recycling, it burns fuel, so it creates GHG emissions. The landfill itself might affect water quality – or land use change.
These indirect effects of human activity are called environmental impacts.

## Slide 8: Impacts come from across a whole life cycle
Notes: And once you start thinking about environmental impacts, you realize they don’t just occur when you are throwing something away or recycling it.

## Slide 9: Impacts come from across a whole life cycle
Notes: Everything that we see as trash comes from somewhere. It was extracted from the earth somehow…

## Slide 10: Impacts come from across a whole life cycle
Notes: … mined, or farmed, or fished, or forested.
Then it was brought to us somehow. We call this stage production. And all of that work creates environmental impacts like GHG emissions, land use change, water use, etc.

## Slide 11: Impacts come from across a whole life cycle
Notes: Then it spends some time in the human environment, where we use it, whatever it is. There are more environmental impacts here. We call this stage “use”.

## Slide 12: Impacts come from across a whole life cycle
Notes: Finally when we are done with it, we either recycle it or dispose of it. We call this stage “end-of-life,” and there are environmental impacts here too.

## Slide 13: We want to reduce the total “life cycle impact”
Notes: The sum of all the impacts is called the “life cycle impact.”
What we want to do, to protect the environment, is to minimize those impacts.
However, there’s a problem – figuring out that impact is not a simple matter.

## Slide 14: Waste Impact Calculator bridges the gap
Notes: The Waste Impact Calculator bridges the gap between these two perspectives.

## Slide 15: Enter WIC
Intended for people who manage or are interested in managing solid waste – government staff, interested nonprofits, etc.
Takes standard weight-based data as input
Outputs estimated life cycle impacts
Allows you to experiment with managing waste different ways
Notes: It is a calculator. WIC takes what you know about solid waste – how many tons of stuff are going to what sorts of places – and figures the life cycle environmental impacts for that stuff.
It also lets you imagine you are handling waste in different ways…. And see how the impacts change. Like maybe you would want to increase composting, or reduce food waste overall.

## Slide 16: A few screens to give you the idea
(switch to app)

## Slide 17: Versions of the Waste Impact Calculator
Web app
R codebase with example
Notes: There are two versions of the calculator.
First, there is a web app. You just saw me using a little bit of the web app, but it has lots of screens. The web app comes pre-loaded with some data sets representing counties in Oregon, and also has an interface where you can enter your own waste data. This is probably the easiest place to start, but you are somewhat limited to the particular analyses the screens have been designed to do.
If you want to go beyond that, the Calculator is also available as a whole code base. If you can program in R, you can take the core files from the project and alter them to suit your own needs. An example analysis is included.

## Slide 18: Stuff you can do with the codebase version
As many scenarios as you want
Your own colors 
Notes: There are two versions of the calculator.
First, there is a web app. You just saw me using a little bit of the web app, but it has lots of screens. The web app comes pre-loaded with some data sets representing counties in Oregon, and also has an interface where you can enter your own waste data. This is probably the easiest place to start, but you are somewhat limited to the particular analyses the screens have been designed to do.
If you want to go beyond that, the Calculator is also available as a whole code base. If you can program in R, you can take the core files from the project and alter them to suit your own needs. An example analysis is included.

## Slide 19: Similarities and differences vis-à-vis WARM
Similarities
Differences
Model impacts of solid waste
Compare scenarios for solid waste management
WIC displays production impacts consistently
WIC has more impact categories, including water use, air particulates, etc.
More simultaneous scenarios
Source of impact factors is Oregon DEQ

## Slide 20: How it works

## Slide 21: Start with solid waste data in its most detailed form
Tons of a specific material going to a specific end-of-life disposition
Material | Tons | Disposition
Steel | 10 | Landfilling
Steel | 15 | Recycling
Notes: Basic element of solid waste data

## Slide 22: For the first combination of material & disposition..
Apply that number of tons to the materials life cycle
Apply an impact factor
Multiply to get an impact
Material | Tons | Life cycle stage | Impact Factor | Impact
Steel | 10 | Production | 4 | 40
Steel | 10 | Use | ?? | 0
Steel | 10 | End-of-life transport | 0.5 | 5
Steel | 10 | End-of-life (landfilling) | 1.5 | 15

## Slide 23: For every subsequent combination
Do the same thing
Material | Tons | Life cycle stage | Impact Factor | Impact
Steel | 15 | Production | 4 | 60
Steel | 15 | Use | ?? | 0
Steel | 15 | End-of-life transport | 0.5 | 7.5
Steel | 15 | End-of-life (recycling) | -2 | -30

## Slide 24: Add up all those detailed impacts as desired
Weight view
Chart: Tons
| Steel
Landfilling | 10
Recycling | 15
Impact view
Chart: Impact
| Steel
Production | 100
End-of-Life Transport | 12.5
End-of-Life | -15

## Slide 25: You can do this for as many materials as you want
Weight view
Chart: Tons
| Steel | Food Waste
Landfilling | 10 | 12
Recycling | 15 | 0
Composting | 0 | 10
Impact view
Chart: Impact
| Steel | Food Waste
Production | 100 | 130
End-of-Life Transport | 12.5 | 4
End-of-Life | -15 | -12

## Slide 26: Details
Notes: Now let’s clarify some details that you might be wondering about.

## Slide 27: Why is the use phase ignored?
Solid waste data tends to be in terms of commodity materials, not products
E.g. “10 tons of steel”
We can’t know what the use was

## Slide 28: Where do we see the benefits of recycling?
In negative values for the end of life stage…
Leading to a lower net impact
These values represent situations where we assume using recycled material prevents production from newly extracted material – or has some other net positive effect
Such assumptions have been challenged
Chart: Impact
| Steel
Production | 100
End-of-Life Transport | 12.5
End-of-Life | -15
Net impact
Zero impact

## Slide 29: Can end-of-life transport be customized?
There are many questions about the role of end-of-life transport in impacts
In WIC, end-of-life transport is from the collection point to the disposal point or first recycling market participant
WIC assumes a standard distance, but custom distances can be entered and the factor will be scaled appropriately.
Standard end-of-life transport factor | Standard distance | Actual distance | Customized end-of-life transport factor
6 | 120 | 40 | 2

## Slide 30: Some more examples

## Slide 31: What does WIC leave out?

## Slide 32: The use phase

## Slide 33: WIC only includes things recorded as solid waste
Notes: Let’s start with an intuitive definition.
Here’s a picture of a municipal trash collection. Notice how the cans of trash and recycling are all clearly separated from the houses? Waste can be defined as the stuff that people get rid of!
That’s the viewpoint of historian Susan Strasser, in her book Waste and Want, and it’s really profound if you dwell on it.

## Slide 34


?
?
?
?
x
Notes: More legalistic definitions of solid waste can be found in statistics from governments and nonprofits. Here’s a chart from the UN that attempts to break down all the different parties or activities that might have stuff to get rid of – that is, who might produce solid waste.
There are commercial operations, like stores, and households. Government statistics usually do include those in what they call solid waste, so I’ll put check marks by those operations.
But all sorts of other operations also have to get rid of stuff. Such as industrial operations, energy production facilities, water treatment plants, and construction sites. Governments differ greatly in whether they include these things in what they call solid waste.
And nobody includes the huge amounts of waste that are generated in agricultural, forestry, and mining operations.

## Slide 35
Notes: That means when you hear the term solid waste, you are usually just hearing about municipal and commercial waste. That’s how the term is used in the Waste Impact Calculator, because that’s how Oregon defines it in its state environmental law.

## Slide 36: Some materials with large impacts are omitted
Notes: As you get more and more into the environmental effects of solid waste, it’s important to remember that there are lots of materials which have a big impact on the environment that solid waste statistics will never tell you about.
Concrete is one example. It’s responsible for a large portion of greenhouse gas emissions planet wide, but the concrete they pour today won’t be in the solid waste stream – if it’s even counted – for a hundred years.
So solid waste is surely related to affluence and consumption, but solid waste doesn’t tell the whole story about how materials and products influence the environment.

## Slide 37: Take-home message:
Solid waste ≠ material consumption
Notes: As you get more and more into the environmental effects of solid waste, it’s important to remember that there are lots of materials which have a big impact on the environment that solid waste statistics will never tell you about.
Concrete is one example. It’s responsible for a large portion of greenhouse gas emissions planet wide, but the concrete they pour today won’t be in the solid waste stream – if it’s even counted – for a hundred years.
So solid waste is surely related to affluence and consumption, but solid waste doesn’t tell the whole story about how materials and products influence the environment.

## Slide 38: Alternative big-picture models
CBEI, USEEIO, EORA, etc.

## Slide 39: Thanks
Martin Brown Martin.Brown@state.or.us